## Slide 1: Welcome to IoT World for SMKDT STUDENT
Content :
What is IoT
What is Blynk app and Arduino IDE
Installing Blynk app and Arduino IDE
Installing ESP32 library and blynk on Arduino IDE
Checking ESP32 work or not using blink code and how to upload
C++ Arduino IDE programming‘s rules
Basic Instruction (analog & digital read&write)
Blynk integration code (turn on off lamp from android)
SMKDT’s IoT Expo
Sundanese Jarvis (ardumeka founder’s expo)
Speaker : Muhammad Husni, S. Pd
Python Programmer
Alumni SMKDT Angkatan 4 (Geist In Vier)

## Slide 2: About me
Name : Muhammad Husni Muttaqin, S. Pd.
Birth date : 5 June 1998
Hometown : Bandung
Current Job : Python programmer at PT Syergie Indoprima
Experiences : - 2019 : Dynamics Positioning System control system engineer on cable ship kalibaru – untung jawa 20Kv cable installation (PT Syergie Indoprima)
- 2019 : Dynamics Positioning System control system engineer on cable ship lampung – pahawang 20Kv cable installation (PT Syergie Indoprima)
- 2020 : Dynamics Positioning System control system engineer on cable ship palapa ring tengah cable maintenance (PT Syergie Indoprima)
- 2021 - 2022 : Electronics and control system engineer for Vent-I (PT Syergie Automa Teknologi)
- 2022 : python programmer

## Slide 3: Ppt + source code on :
https://github.com/muhammadhusni777/SMKDT-IOT-CLUB

## Slide 4: My achievement on electronics and IoT World
- 3 rd winner on International innovative IoT idea 2017

## Slide 5: My achievement on electronics and IoT World
- Metro tv award : scientific problem solving on pandemic (Vent-I ITB Team)

## Slide 6: Teaching experience : Elektronika Pesawat Udara SMK12 Bandung

## Slide 7: Teaching experience : Founder Ardumeka

## Slide 8: Current Project

## Slide 9: Current projects
Find control equation for new generation ship propeller

## Slide 11: What is IoT

## Slide 12: What is Blynk app
Go to playstore, search blynk IoT, install Blynk legacy

## Slide 13: What is Arduino Ide
https://www.arduino.cc/en/software

## Slide 14: Install COM driver
Install CP2102 (https://exploreembedded.com/wiki/Cp2102_Usb-to-Serial_Driver_Installation)
Install CH340 (https://kelasrobot.com/cara-install-usb-driver-ch340g-ch340-untuk-arduino )

## Slide 15: Install ESP32 board library
https://randomnerdtutorials.com/installing-the-esp32-board-in-arduino-ide-windows-instructions/
Json file : https://dl.espressif.com/dl/package_esp32_index.json

## Slide 16: Install Blynk library arduino
Common problem solving : https://kelasrobot.com/solved-cara-mengatasi-error-login-timeout-blynk/

## Slide 17: Basic Instruction (analog & digital read&write)
Analog read : read 0-3.3 volt (ESP32), read 0-5 volt (Arduino nano/mega/uno)
Analog Write : give 0-3.3 volt (ESP32, give 0-5 volt (Arduino nano/mega/uno)
Digital read : read 0 AND 3.3 volt (ESP32), read 0 AND 5 volt (Arduino nano/mega/uno)
Digital Write : give 0 AND 3.3 volt (ESP32, give 0 AND 5 volt (Arduino nano/mega/uno)

## Slide 19: Analog Read
void setup() {
Serial.begin(9600);
}
void loop() {
int sensorValue = analogRead(A0);
Serial.println(sensorValue);
}

## Slide 20: trap 

## Slide 21: Analog Write (ESP32)

## Slide 22: Analog Write (Arduino microcontroller)
Int lampu = 6;
void setup() {
pinMode(lampu, OUTPUT);
}
void loop() {
analogWrite(lampu, 0);
delay(1000);
analogWrite(lampu, 255);
delay(1000);
}

## Slide 23: Digital write
Int lampu = 2;
void setup() {
pinMode(lampu, OUTPUT);
}
void loop() {
digitalWrite(lampu, HIGH);
delay(1000);
digitalWrite(lampu, LOW);
delay(1000);
}

## Slide 24: Digital read
int pushButton = 5;
void setup() {
Serial.begin(9600);
pinMode(pushButton, INPUT_PULLUP);
}
void loop() {
int buttonState = digitalRead(pushButton);
Serial.println(buttonState);
delay(1); // delay in between reads for stability
}

## Slide 25: Blynk integration code (turn on off lamp from android)
Blynk_benchmark

## Slide 26: SMKDT’s IoT Expo #1 (May’22)
Dorm Smart lamp
Dorm windows smart security system
Dorm smart water heater
Dorm smart Fan
Dorm Smart garden
Dorm smart water fill
Dorm smart Bin
Hand gesture lamp switch (ardumeka founder’s + SMKDT ALLSTAR expo)
Sundanese Jarvis (ardumeka founder’s expo)

## Slide 27: Stand 01 : Dorm Smart lamp

## Slide 28: Stand 01 : Dorm Smart lamp
Objective :
- digitalWrite from blynk 3 or more objects (lamp)

## Slide 29: Stand 02 : Dorm windows smart security system

## Slide 31: Stand 02 : Dorm windows smart security system
Objective :
Digital Read three or more object and send to blynk app
Give notification to blynk

## Slide 32: Stand 03 : Dorm smart water heater

## Slide 33: Stand 03 : Dorm smart water heater
Objective :
Send target value to esp from blynk
Receive DHT 11/22 value from esp to blynk
Make if else statement to control the heater (turn off if sensor value above target value and vice versa)

## Slide 34: Optional :
https://create.arduino.cc/projecthub/dirakit_indonesia/saveyourchicken-b7da4d

## Slide 35: Stand 04 :Dorm smart Fan

## Slide 36: Stand 04 :Dorm smart Fan
Objective :
- digitalWrite from blynk 3 or more objects (fan)

## Slide 38: Stand 05 : Dorm Smart garden

## Slide 39: Stand 05 : Dorm Smart garden
Objective :
Send target value to esp from blynk (soil moisture level)
Receive soil value from esp to blynk
Make manual mode. If blynk button turn on the pump will turn on
Make automatic mode. if else statement to control the pump (turn off if sensor value above target value and vice versa)

## Slide 40: Stand 06 : Dorm smart water fill

## Slide 41: Stand 06 : Dorm smart water fill
Objective :
Send target value to esp from blynk (water level)
Receive water level from esp to blynk
Make manual mode. If blynk button turn on the pump will turn on
Make automatic mode. if else statement to control the pump (turn off if sensor value above target value and vice versa)

## Slide 42: Stand 07 :Dorm smart Bin

## Slide 43: Stand 07 :Dorm smart Bin
Objective :
Read proximity sensor
Trigger servo using proximity sensor
Send count number to blynk app

## Slide 44: Stand 08 : Hand gesture lamp switch (ardumeka founder’s + SMKDT ALLSTAR expo)

## Slide 45: Stand 09 : Sundanese Jarvis (ardumeka founder’s expo )

## Slide 46: Sundanese Jarvis (ardumeka founder’s expo )
COMING SOON

## Slide 47: Never give up guys 